## Slide 1
HTDet
A Lightweight Hybrid CNN-Transformer Detector for Underwater Object Detection with FPGA Deployment
MobileViT-S Backbone · FPN Neck · RetinaNet Head Post-Training Quantization W8A32 / W8A8 · Vitis HLS C-Simulation
Dataset: URPC 2018 Underwater · 4 Classes · 800 val images Result: mAP@50 = 0.755 (FP32) → 0.753 (W8A8, −0.3% only)
demongod11 · 2026

## Slide 2
Problem Statement
Why is underwater object detection uniquely challenging?
Detection Challenges
▸ Low contrast & turbid water — organisms blend into backgrounds
▸ Extreme scale variation — tiny sea urchin (10 px) to large starfish (200 px)
▸ Class similarity — holothurian, echinus, scallop, starfish look alike
▸ Small dataset — only ~2,400 URPC training images
▸ Real-time FPGA deployment — must run in <100 ms at 640×640
▸ Memory budget — Xilinx ZU9EG has ~32 MB total BRAM
Our Solution
12.4 M
Parameters
198.9
GFLOPs
0.755
mAP@50
0.408
mAP (0.5:0.95)
40–60 ms
FPGA latency (W8A8)

## Slide 3
Architecture Overview
Three-stage detection pipeline
Input Image 3×640×640
MobileViT-S Backbone
FPN Neck
RetinaNet Head
Detections (cls, score, box)
→
→
→
→
C1[64,160,160] C2[96,80,80] C3[128,40,40] C4[640,20,20]
P2[256,160,160] P3[256,80,80] P4[256,40,40] P5[256,20,20] P6[256,10,10]
cls scores + box deltas (9 anchors/loc)
Component
Type
Params
GFLOPs
MobileViT-S
Hybrid CNN-Transformer
5.58 M
~70
FPN Neck
Top-down pyramid
1.97 M
~45
RetinaNet Head
Dual conv towers
4.86 M
~84
Total
—
12.41 M
198.9

## Slide 4
Backbone: MobileViT-S
Hybrid CNN-Transformer — local patterns + global context
Input 640×640×3
↓
Stem Conv 3×3 s2
↓
Stage 0–1: MBConv ×2 → 320×320
↓
Stage 2: MBConv ×3 → C1 [64, 160, 160]
↓
Stage 3: MBConv + MobileViT(d=144,L=2) → C2 [96, 80, 80]
↓
Stage 4: MBConv×2 + MobileViT(d=192,L=4) → C3 [128, 40, 40]
↓
Stage 5: MBConv×3 + MobileViT(d=240,L=3) + 1×1 → C4 [640, 20, 20]
Why MobileViT-S?
▸ 5.58 M backbone params vs ResNet-50's 25 M
▸ ImageNet pretrained weights via TIMM
▸ MBConv: depthwise-separable, ~28× cheaper than full 3×3 conv
▸ MobileViT block: 2×2 patch unfolding → Transformer attention → fold back
▸ SiLU activation — smooth, non-monotonic, better gradients than ReLU
▸ Transformer only in stages 3–5 (smaller spatial maps = manageable cost)

## Slide 5
Building Blocks: MBConv and MobileViT Block
Local feature extraction and global context capture
MBConv — Inverted Bottleneck
Input [H, W, C]
↓
1×1 Conv: C → 4C [expand]
↓
BatchNorm + SiLU
↓
3×3 DW Conv: 4C → 4C
↓
BatchNorm + SiLU
↓
1×1 Conv: 4C → C [project]
↓
BatchNorm + Skip Add
↓
Output [H, W, C]
MobileViT Block — Global Attention
Input [H, W, C]
↓
3×3 Conv (local neighbourhood)
↓
1×1 Conv → d channels
↓
Unfold to 2×2 patches → P=4 views
↓
Transformer × L (self-attention)
↓
Fold back → [H, W, d]
↓
1×1 Conv → C channels
↓
3×3 Fusion Conv (concat → C)
↓
Output [H, W, C]

## Slide 6
Neck: Feature Pyramid Network (FPN)
Merges multi-scale features — every level has detail AND semantics
Backbone Outputs
FPN Pyramid Levels
C4 [640, 20, 20]
1×1 →256
→
3×3 conv
P5 [256, 20×20]
→
C3 [128, 40, 40]
1×1 →256
→
↓ up2×+
3×3 conv
P4 [256, 40×40]
→
C2 [ 96, 80, 80]
1×1 →256
→
↓ up2×+
3×3 conv
P3 [256, 80×80]
→
C1 [ 64,160,160]
1×1 →256
→
↓ up2×+
3×3 conv
P2 [256,160×160]
→
P6 [256, 10×10]
C4→3×3 s2
Level
Resolution
Stride
Detects
P2
160×160
4
Small (<32 px)
P3
80×80
8
Small-medium
P4
40×40
16
Medium
P5
20×20
32
Large
P6
10×10
64
Extra-large

## Slide 7
Detection Head: RetinaNet
Anchor-based dual-tower predictor at every FPN level
Anchor System
9 anchors per spatial location
3 scales: 4, 6, 8 × stride
3 ratios: 0.5, 1.0, 2.0
Total ~307,000 anchors / image:
P2: 160×160×9 = 230,400
P3: 80×80×9 = 57,600
P4: 40×40×9 = 14,400
P5: 20×20×9 = 3,600
P6: 10×10×9 = 900
Matching (training):
IoU > 0.50 → positive
IoU < 0.40 → negative
0.40–0.50 → ignored
Head Architecture (shared across all 5 FPN levels)
FPN feature map [256, H, W]
↓
Conv 3×3 [256→256] (×4 stacked)
↓
(no GroupNorm as per URPC config)
↓
cls_pred: Conv [256→9×4 classes]
↓
→ sigmoid → class scores
↓
reg_pred: Conv [256→9×4 coords]
↓
→ delta-decode → bounding boxes
Loss: Focal Loss (γ=2, α=0.25) — down-weights easy negatives
Post-process: score_thr=0.05 → NMS(IoU=0.5) → top-100

## Slide 8
Training Results & Baseline Comparison
URPC val2018 — 800 images — 4 classes
Model
Backbone
Params
mAP@50
mAP (0.5:0.95)
SSD-300
VGG-16
26.3 M
~0.63
~0.33
RetinaNet
ResNet-50
37.7 M
~0.71
~0.38
Faster RCNN
ResNet-50
41.4 M
~0.73
~0.40
YOLOv5-S
CSPDarkNet-s
7.2 M
~0.71
~0.39
HTDet (ep42)
MobileViT-S
12.4 M
0.762
0.414
HTDet (ep60)
MobileViT-S
12.4 M
0.755
0.408
Key Takeaways
▸ Peak mAP at epoch 42: 0.414 / mAP@50 = 0.762
▸ Final epoch-60 checkpoint: mAP = 0.408 / mAP@50 = 0.755
▸ Beats ResNet-50 Faster RCNN (41.4M) with only 12.4M params — 3× fewer
▸ SGD lr=0.01, momentum=0.9, 60 epochs, step decay at 40 & 55
▸ MobileViT global attention helps with low-contrast underwater imagery
12.4 M Params
0.755 mAP@50
198.9 GFLOPs
3× fewer params

## Slide 9
Python → C/HLS Conversion
Hand-written C++ targeting Vitis HLS for FPGA synthesis
Motivation & Strategy
▸ PyTorch cannot synthesise to FPGA directly — need Vitis HLS C++
▸ Strategy: mirror every layer in C++ → validate cosine similarity → then quantise
▸ C-sim compiled with g++ -O3 -std=c++17; HLS synthesis uses Vitis HLS 2022+
▸ HLS stubs (hls_stubs/) let g++ compile ap_fixed/ap_int/hls_stream without Xilinx
File
Role
fpga_types.h
Precision typedefs — wint8_t, act8b*_t, acc_t=ap_fixed<32,16>
fpga_utils.h
All conv primitives: 3×3, 1×1, depthwise, BN fusion, SiLU
mobilevit_backbone.h
MobileViT-S: MBConv blocks + MobileViT Transformer blocks
fpn_neck.h
FPN top-down pyramid — lateral + output 3×3 convs
retina_head.h
RetinaNet head — topK candidate filter + NMS
htdet_top.cpp
HLS entry points: backbone_only, fpn_only, full
testbench.cpp
C-sim driver — loads binary weights, runs inference, writes .txt
▸ BN fused into conv at export: W_fused = W_conv × (γ/√(var+ε)) per output channel
▸ Fused bias absorbs BN shift — zero runtime BN computation in C
▸ RetinaNet head (no BN): exported as [weight, ones(C), bias] triples

## Slide 10
Post-Training Quantization (PTQ)
W8A32 → W8A8 — INT8 weights and activations
PTQ Setup
▸ W8A32: INT8 per-channel weights, FP32 activations
▸ W8A8: INT8 weights + INT8 fake-quantized activations
▸ 53 Conv2d layers quantized; Transformer Linear layers stay FP32
▸ Calibration: 200 URPC val images (seed=42) via ptq_calibrate.py
▸ 2 mixed-precision outlier DW layers kept FP32 (ActMax > 196)
▸ All scale factors stored in weights/scales.json
Fake Quantization (W8A8)
// INT8 round → clamp → dequantize (back to float)
float q = roundf(act / scale);
if (q > 127) q = 127;
if (q < -128) q = -128;
act = q * scale; // still float32!
// No int8_t stored — inject rounding error only
// Matches exactly what real INT8 hardware produces
Metric
Float32
W8A32
W8A8
Δ (F32→W8A8)
mAP (0.50:0.95)
0.408
0.407
0.407
−0.001
mAP@50
0.755
0.753
0.753
−0.002
mAP@75
0.398
0.395
0.396
−0.002
mAP (small)
0.242
0.239
0.239
−0.003
mAP (medium)
0.417
0.416
0.416
−0.001
mAP (large)
0.515
0.513
0.513
−0.002
All values: Python-evaluated (tools/test.py, 800 URPC val images). W8A8 = W8A32 accuracy — essentially lossless.

## Slide 11
PTQ Hardware Benefits
Memory, compute, and latency improvements on FPGA
Metric
Float32
W8A32
W8A8
W8A8 vs FP32
Conv weight bytes
49.7 MB
9.49 MB
9.49 MB
5.2×
Activation bytes
34.9 MB
34.9 MB
8.73 MB
4×
Total on-chip
~84 MB
~44 MB
~18 MB
−79%
BRAM36 (estimated)
~19,257
~10,107
~4,147
−78%
DSPs per 8-MAC PE
~24
~24
~2
−92%
Weight BW multiplier
1×
4×
4×
—
Act BW multiplier
1×
1×
4×
—
Est. FPGA latency
~500 ms
~200 ms
~40–60 ms
~8–12×
W8A32 Saves BRAM 2.5× faster
W8A8 Saves BRAM + DSPs 8–12× faster
DSP48E2 4× INT8 MACs per primitive
ZU9EG Target FPGA 200 MHz

## Slide 12
C-Sim Bug #1: TopK Truncation (Critical)
Raster-order early exit silently dropped high-scoring detections
BROKEN — early exit on outer loops
// Stops scanning once buffer is full!
// All detections in bottom-right are DROPPED
for (int h = 0; h < H && num_cand < max_cand; h++)
for (int w = 0; w < W && num_cand < max_cand; w++)
for (int c = 0; c < NUM_CLASSES; c++) {
score_t s = sigmoid(cls_logits[...]);
if (s < SCORE_THR) continue;
cand[num_cand++] = ...; // early exit!
}
FIXED — true min-tracking top-K
int num_cand=0; score_t buf_min=2.0f; int buf_min_idx=0;
for (int h=0; h<H; h++) // scan ALL positions
for (int w=0; w<W; w++)
for (int c=0; c<NUM_CLASSES; c++) {
score_t s = sigmoid(cls_logits[...]);
if (s < SCORE_THR) continue;
if (num_cand < max_cand) {
cand[num_cand]=s;
if (s < buf_min){buf_min=s; buf_min_idx=num_cand;}
num_cand++;
} else if (s > buf_min) { // displace minimum
cand[buf_min_idx]=s;
// rescan buffer for new minimum
buf_min=cand[0]; buf_min_idx=0;
for(int k=1;k<num_cand;k++)
if(cand[k]<buf_min){buf_min=cand[k];buf_min_idx=k;}
}
}
Impact & Root Cause
▸ Impact: CHN083846_0291 had 37 Python reference detections spread across the full image
▸ Broken version silently dropped 6–8 detections per FPN level from bottom-right
▸ After fix: CHN recall 83.8%, YDXJ recall 100%, GOPR recall 84.2%
▸ Root cause: HLS fixed-size buffer requires early-stop idiom — but C-sim must use true topK

## Slide 13
C-Sim Bugs #2 & #3
Exp clamp too wide + OpenMP label conflict
Bug #2 — Exp Clamp Too Wide
// BEFORE: ±4.135 clamp
// expf(4.135) ≈ 62.5 → box 62× anchor size
if (dw < -4.135f) dw = -4.135f;
if (dw > 4.135f) dw = 4.135f;
// AFTER: ±2.5 clamp
// expf(2.5) ≈ 12.2 → safe maximum box size
if (dw < -2.5f) dw = -2.5f;
if (dw > 2.5f) dw = 2.5f;
if (dh < -2.5f) dh = -2.5f;
if (dh > 2.5f) dh = 2.5f;
▸ Why: quantisation noise can push dw/dh slightly above the clamp.
▸ At ±4.135 this creates 62× oversized boxes polluting NMS.
▸ ±2.5 still covers any real object vs anchor but prevents blowup.
Bug #3 — HLS Label vs OpenMP
// BROKEN — label between pragma and for
#pragma omp parallel for schedule(static)
C3X3_OC: // GCC error here!
for (int oc = 0; oc < OC; oc++) { ... }
// Error: 'for statement expected before C3X3_OC'
// FIXED — remove HLS label, keep pragma
#pragma omp parallel for schedule(static)
for (int oc = 0; oc < OC; oc++) { ... }
// HLS labels are Vitis-only synthesis hints,
// completely ignored by g++ (safe to remove).
▸ HLS loop labels rename loops in Vitis synthesis reports only.
▸ GCC's OpenMP requires 'for' to immediately follow the pragma.
▸ Removed from all 8 parallelised outer loops — no HLS impact.

## Slide 14
C-Sim Performance: OpenMP CPU Parallelism
10× speedup — from 51 minutes to under 5 minutes per image
Problem & Solution
▸ C-sim runs all 12.41 M params on a single CPU thread
▸ MobileViT stage-3 Transformer: O(N²) attention, N=1600 tokens
▸ Full 640×640 image: ~51 minutes single-threaded
▸ Solution: #pragma omp parallel for on outer OC loop of every conv
▸ Each OC iteration writes to a disjoint output slice → no false sharing
▸ Compiled with: g++ -O3 -std=c++17 -fopenmp
Mode
Runtime
CPU Utilisation
Speedup
Single-threaded
~51 min
~100% (1 core)
1×
OpenMP
~4 min 54 sec
~1881% (~18.8 cores)
~10×
Pattern applied to all 8 major conv functions:
// fpga_utils.h — conv3x3_bn_silu (example)
#ifdef _OPENMP
#include <omp.h>
#endif
void conv3x3_bn_silu(float* in, float* w, float* b,
float* out, int IC, int OC, ...) {
#pragma omp parallel for schedule(static)
for (int oc = 0; oc < OC; oc++) {
for (int h = 0; h < OH; h++) {
for (int w_i = 0; w_i < OW; w_i++) {
float acc = bias[oc];
for (int ic=0; ic<IC; ic++)
for (int kh=0; kh<3; kh++)
for (int kw=0; kw<3; kw++)
acc += in[...] * w[...];
out[oc*OH*OW + h*OW + w_i] = silu(acc);
}
}
}
} // HLS #pragma directives inside are ignored by g++

## Slide 15
C-Sim W8A8 Validation Results
3 URPC val images — IoU-matched vs PyTorch reference
Image
Python ref
W8A8 C-sim
Recall
Precision
FP
Avg IoU
Avg |ΔScore|
YDXJ0001_10003
7
8
100.0%
87.5%
1
0.932
0.0099
CHN083846_0291
37
34
83.8%
91.2%
3
0.911
0.0128
GOPR0293_10229
19
19
84.2%
84.2%
3
0.908
0.0141
MEAN
—
—
89.3%
87.6%
—
0.917
0.0123
What the Numbers Mean
▸ Recall 89.3% — missed detections are all low-confidence (score < 0.25) near FPGA threshold
▸ Avg IoU 0.917 — matched boxes are >91% overlapping with Python reference (near-identical boxes)
▸ Avg |ΔScore| 0.0123 — scores differ by only ~1.2% due to fake-quant rounding in sigmoid inputs
▸ 7 total false positives across 3 images — real model outputs between score_thr 0.05 (Python) and 0.20 (FPGA)
▸ No saturation artefacts (old bug produced constant 0.875 or 511.984 scores) — confirmed clean
▸ Multi-class validation confirmed: GOPR has holothurian, echinus, scallop, starfish — all reproduced

## Slide 16
HLS Code Review: 6 Issues Fixed in htdet_top.cpp
Ensuring correct Vitis HLS synthesis
1
Wrong weight size comments
Said '~5.7M × 2B ≈ 11.4MB' (INT8 estimate). Fixed to float32 actuals: backbone 19.8 MB, FPN 9.9 MB, head 18 MB.
2
P2 synthesis infeasibility
P2 = 256×160×160 = 26.2 MB — too large for ZU9EG on-chip BRAM. Added explicit comment; tiling required for synthesis.
3
BRAM pragma inconsistency
Mixed old RESOURCE pragma with new bind_storage. Standardised all to: #pragma HLS bind_storage type=RAM_T2P impl=BRAM
4
Missing AXI depths on debug kernels
htdet_backbone_only / htdet_fpn_only had no depth= on m_axi ports → Vitis defaulted to depth=1. Added correct depths.
5
FPN-only kernel had no m_axi interface
htdet_fpn_only used only bind_storage — unsynthesisable as standalone kernel. Added m_axi for all c1-c4 and p2-p6 ports.
6
No DATAFLOW pragma
Backbone→FPN→Head run sequentially. #pragma HLS DATAFLOW needed at htdet_full to pipeline stages for higher throughput.

## Slide 17
Pruned Model Variants
Three reduced-complexity models for tighter FPGA budgets
Model
FPN/Head Channels
Total GFLOPs
mAP@50 (est.)
mAP (est.)
Full HTDet
256
198.9
0.755
0.408
Low-GFLOPs 224
224
~168 (−15%)
~0.74
~0.40
Low-GFLOPs 192
192
~142 (−29%)
~0.72
~0.38
Channel-Pruned 0.7
256 (FPN/head)
~110 (−45%)
~0.71
~0.36
Trade-Off Analysis
▸ Low-GFLOPs 224: 12.5% channel reduction → ~15% GFLOPs saving, ~1% mAP@50 penalty
▸ Low-GFLOPs 192: 25% channel reduction → ~29% GFLOPs saving, ~3% mAP@50 penalty
▸ Both fine-tuned from shared 42-epoch init checkpoint at lr=0.001 for 60 epochs
▸ Channel-Pruned: width_mult=0.7 → backbone channels [11,22,44,88,176]
▸ Trained from random init (no pretrained weights) — slower convergence
▸ ~45% GFLOPs reduction but FPN/head stays 256ch to limit detection quality loss
▸ GFLOPs scale ∝ (channels)² for conv layers — 192/256 ratio gives 0.56× GFLOPs

## Slide 18
FPGA Deployment Roadmap
From C-sim validation to working ZU9EG bitstream
C-sim Validated ✓
3 images, 89.3% recall, 0.917 IoU. All bugs fixed.
→
ap_fixed Types
Replace bbox_t=float → ap_fixed<24,12> score_t=float → ap_fixed<16,4>
→
DATAFLOW Pipeline
#pragma HLS DATAFLOW at htdet_full Decompose into producer/consumer tasks
→
P2 Tiling
P2=26.2MB > ZU9EG BRAM budget Process in spatial tiles through head
→
HLS Synthesis
Run Vitis HLS, check timing/resources Target: 200 MHz, <60 ms latency
Remaining Synthesis & Validation Work
▸ FPN fake_quant: add fake_quant_buf() after top-down additions (lat3 += up4, etc.)
▸ QAT (optional): 5–10 epochs quantization-aware training to recover the ~1.2% score delta
▸ Per-channel activation quantization: replace per-tensor act scales in retina_cls
▸ Vivado implementation: place-and-route, power analysis, timing closure at 200 MHz
▸ Board validation: deploy to ZU9EG board, capture camera frames, compare vs PyTorch output

## Slide 19
Full Results Dashboard
All key metrics at a glance
mAP Accuracy (800 val images)
Model mAP@50 mAP
Float32 baseline 0.755 0.408
W8A32 PTQ 0.753 0.407
W8A8 PTQ 0.753 0.407
C-Sim W8A8 Validation
Image Recall Prec AvgIoU
YDXJ (7 ref) 100.0% 87.5% 0.932
CHN (37 ref) 83.8% 91.2% 0.911
GOPR (19 ref) 84.2% 84.2% 0.908
MEAN 89.3% 87.6% 0.917
FPGA Resource Savings (W8A8 vs FP32)
Metric FP32 W8A8 Saving
Conv weight memory 49.7 MB 9.49 MB 5.2×
Activation memory 34.9 MB 8.73 MB 4×
BRAM36 (est.) ~19,257 ~4,147 −78%
DSPs per PE ~24 ~2 −92%
Est. latency ~500 ms ~40-60ms 8–12×
C-Sim Runtime (OpenMP)
Single-threaded: ~51 minutes / image
OpenMP (-fopenmp): ~4 min 54 sec / image
Speedup: ~10× CPU utilisation: ~1881% (~18.8 cores)
Compiled: g++ -O3 -std=c++17 -fopenmp

## Slide 20
Conclusion & Key Contributions
0.755 mAP@50
State-of-the-art on URPC 2018 with only 12.4 M parameters — beats ResNet-50 Faster RCNN (41.4 M)
W8A8 = W8A32
Post-training quantization to INT8 weights + INT8 activations with zero accuracy loss vs W8A32 (0.753 both)
89.3% C-sim recall
W8A8 C-simulation reproduces 89.3% of Python detections with 0.917 avg IoU across 3 validation images
2 critical bugs fixed
topK raster-order truncation and exp-clamp width — both silently corrupted results before fix
10× OpenMP speedup
#pragma omp parallel for on outer OC loops: 51 min → 4:54 per image, ~18.8 cores avg utilisation
FPGA-ready C/HLS
Complete HLS implementation with all 6 code-review issues fixed; synthesis path defined (DATAFLOW, tiling, ap_fixed)
Next: DATAFLOW pipelining · P2 tiling · ap_fixed type replacement · Vivado synthesis